## Slide 1: Recent Research in Water Use and Conservation for Nursery and Greenhouse Production
Joshua Knight
Extension Associate, Nursery Crop Production
Department of Horticulture
University of Kentucky
http://NCER.ca.uky.edu
http://cleanwater3.org/

## Slide 2
Water conservation in the Ohio River Valley? (4m)
    Army Corps of Engineers 2017 Report on Climate Change
USDA National Survey Results (2m)
    What are Nursery Growers using?
    What practices and technologies have they heard of?
How are they being compared? (20m)
    Understanding Water Footprint
Technologies/Practices (20m)
    Conservation vs Remediation vs Recycling
    Ponds / Managing Runoff
    Filtration Systems

## Slide 3
Army engineers warn of brutal future for Ohio River region from climate change
Louisville Courier Journal - Published 11:10 a.m. ET Nov. 30, 2017
US Army Corps of Engineers Report (321 pages):
https://NCER.ca.uky.edu/research
Increased Variability of Precipitation
Ohio River Basin is historically “water-rich” with droughts and major flooding events considered “isolated”
Droughts | Major Flooding Events
1988 | 1997
2002 | 2010
2007 | 2011

## Slide 5
Percent Change Streamflow
Annual - Average
Time Period
2011-2040
Compared to 1952-2001

## Slide 6
Percent Change Streamflow
March - Average
Time Period
2011-2040
Compared to 1952-2001

## Slide 7
Percent Change Streamflow
October - Average
Time Period
2011-2040
Compared to 1952-2001

## Slide 8
Percent Change Streamflow
Annual - Maximum
Time Period
2011-2040
Compared to 1952-2001

## Slide 9
Percent Change Streamflow
Annual - Minimum
Time Period
2011-2040
Compared to 1952-2001

## Slide 10
Percent Change Streamflow
March – Maximum
Time Period
2011-2040
Compared to 1952-2001

## Slide 11
Percent Change Streamflow
March – Minimum
Time Period
2011-2040
Compared to 1952-2001

## Slide 12
Percent Change Streamflow
October - Maximum
Time Period
2011-2040
Compared to 1952-2001

## Slide 13
Percent Change Streamflow
October - Minimum
Time Period
2011-2040
Compared to 1952-2001

## Slide 14: Summary until 2040…
Overall ~10% higher streams across KY throughout year
Not necessarily even, potential for periods of
  Prolonged drought
  Excessive precipitation
More water, but it might not come when we need it.
Higher variability north of Ohio River!

## Slide 15: After 2040…
Variability is more extreme!
October Min
October Max

## Slide 16
Figure 10-4: Distribution of Current Water Supply Reservoirs in Cultivated Crop Areas
More irrigation/agriculture ponds in KY?

## Slide 17: SCRI Water3 – National INTERVIEW RESULTS

## Slide 18
Chart: 
| Male | Female
Gender | 73.6 | 26.4
Chart: 
| 18-24 | 25-34 | 35-44 | 45-54 | 55-64 | 65-74 | 75+
Age | 0.8 | 4.7 | 10.9 | 20.9 | 42.6 | 16.3 | 3.9
Chart: 
| $10,000-$99,999 | $100,000-$499,999 | $500,000-$999,999 | $1,000,000-$9,999,000 | $10,000,000+
Gross Annual Sales | 44.2 | 14 | 7.8 | 20.2 | 14
Chart: 
| High School/GED | Some College | 2-Year Degree | 4-Year Degree | Graduate or Professional Degree
Education Level | 5.4 | 19.4 | 12.4 | 35.7 | 27.1

## Slide 19: Water sources
Chart: 
| Private supply - well | Public supply - municipal | Private supply - irrigation pond | Private supply - rainfall capture into tank | Public supply - river & lake | Private supply - rainfall capture onto roofs
Column1 | 0.533 | 0.345 | 0.183 | 0.071 | 0.036 | 0.03

## Slide 20: Use of Treatment Technologies
Chart: 
| Vegetated buffer/riparian buffer for sediment and nutrient removal | Mechanical filters (rapid sand, rotating drum) for particulate removal | Chemical treatment (ozone, chlorine, hydrogen peroxide, etc.) of water for pathogen removal | Vegetated channel for sediment/nutrient removal | Filter socks for sediment removal | Physical treatment (UV, membrane, etc.) of water for pathogen removal | Constructed wetlands for nutrient and pesticide removal | Activated carbon for chemical removal | Floating wetlands for nutrient removal | Bioreactors for pesticides and nitrogen removal | Carbon/denitrification walls for nitrogen removal | Algal turf scrubbers for pathogen removal
 | 23.9 | 23.9 | 22.3 | 18.8 | 15.2 | 12.2 | 11.2 | 8.1 | 3 | 2.5 | 0.5 | 0

## Slide 21: Use of Conservation Technologies
Chart: 
| Drip irrigation | Rain water capture | Water reuse | Micro irrigation | Soil moisture sensors | Climate based irrigation | Sub irrigation | Irrigation audit
Series 1 | 58.4 | 44.7 | 34.5 | 23.4 | 16.2 | 14.7 | 12.2 | 5.6



## Slide 22: Understanding Water Footprint
http://CleanWateR3.org/

## Slide 23: Water Footprint
Footprint -> IMPACT
Similar in basic concept to a Carbon Footprint / Ecological Footprint

## Slide 24: Water Footprint
“Consumptive Use” of water is defined by impact.
Water used for one purpose cannot be used for another purpose at the same time.
Ex. Captured rainfall runoff that has evaporated behind a dam cannot flow downstream and provide habitat.

## Slide 25: Relevant or Competitive uses of water…
Irrigation
Drinking water
Ecological Requirements
- Dilution of pollutants
- Habitat support
ex. aquatic animals, vegetation
Water Footprint

## Slide 26: Is All Consumptive Water Use Equal?
(mostly) No!
Critical Factors:
  Location
  Time of Year
BUT, comparisons between geographic locations should include unweighted Water Footprint volumes.

## Slide 27: Selected Water Scarcity Indices (2011)
A Water Scarcity Index is a ratio equal to
CONSUMPTIVE WATER USE
AVAILABILITY

## Slide 28: Purpose of Water Footprint Analysis
International Standard
&
Broad Application

## Slide 29: Purpose of Water Footprint Analysis
International Standard
Due to international trade,
freshwater is becoming a global resource.
&
Consumers are spatially disconnected
from water resources.

## Slide 30
Virtual water balance per country and direction of gross virtual water flows related to trade in agricultural and industrial products over the period 1996-2005. Only the biggest gross flows (> 15 Gm3 /yr) are shown; the fatter the arrow, the bigger the virtual water flow.

## Slide 31: Purpose of Water Footprint Analysis
International Standard
Not a stick to beat on water by consumers or producers, but rather a method to analyze consumptive water use and ultimately
make practical improvements.

## Slide 32: Purpose of Water Footprint Analysis
Broad Application
Water footprint can allow comparisons
Companies
Products
Commodities
Communities
Individuals
Comparing Water Footprint
Smartphone 240 gallons
Cotton T-shirt 26 gallons
Cup of Coffee 35 gallons
Direct Consumption 27 gallons per day
-washing, cleaning, etc.
Plastic Bottle (1 pint) 1.4 gallons

## Slide 33: How it works… Basic Water Footprint Calculation in Nursery Production
Embodied WF
Green WF
Grey WF
+ Blue WF
Total Water Footprint

## Slide 34: How it works… Basic Water Footprint Calculation in Nursery Production
Embodied WF = Weighted volume of water required for fabrication of inputs
Ex. for field production phase of holly in a #3 container…
Injection molded HDPE plastic container
= 0.534 Gallons (weighted)
Herbicides (total)
= 0.262 Gallons (weighted)
….
Total Embodied WF
= ~ 4.2 Gallons (weighted)

## Slide 35: Basic Water Footprint
Green WF = water used directly during atmospheric events
Calculated as
Volume of irrigation events avoided due to precipitation

## Slide 36
Grey WF is “simple”:
Measure or estimate volume and pollutant load of discharges
Aside from metered additions, Blue WF is complex:
How much rainfall runoff is there to capture?

## Slide 37: How? – Calculating WF
Interview Grower
Complete Checklist
Get Climate Data (30-Y normals)
Calculate Green WF
Calculate Grey WF
Model Captured Rainfall Runoff
Calculate Blue WF

## Slide 38: How? – Calculating Water Footprint
How much of typical rainfall is caught?
Soil
Type
Flow Length
Land Cover
Rainfall
Intensity
Slope

## Slide 39: Calculating Blue WF
Find location
Physical address
or
GPS Coordinates

## Slide 40: How? – Calculating WF
Define production / irrigated area
Models tell us how much runoff can be expected from given rainfall and irrigation

## Slide 41: How? – Calculating WF
Define water reservoirs
100% of rainfall captured in reservoir

## Slide 42: How? – Calculating WF
Find boundaries of catchment
  Elevation map
  Find Flows
  Boundaries

## Slide 43: How? – Calculating WF
Find boundaries of catchment
  Elevation map
  Find Flows
  Boundaries

## Slide 44: How? – Calculating WF
Find boundaries of catchment
  Elevation map
  Find Flows
  Boundaries

## Slide 45: How? – Calculating WF
Define land cover*
Trees/woods, grasses
*only necessary for unengineered areas

## Slide 46: How? – Calculating WF
Find soil drainage types*
*only necessary for unengineered areas

## Slide 47: Rainfall Intensity (monthly)
Rainfall intensity estimated from 30-year normals (1981 – 2010)
Rainfall (inches) 30-yr average | 3.33 | 3.01
Rainfall events => 1 inches | 0.8 | 0.9
Rainfall events => 0.5 inches | 2.6 | 2.4
Rainfall events => 0.1 inches | 6.5 | 5.9
Rainfall events => 0.01 inches | 10.1 | 9.6
Jan
Feb

## Slide 48
Total Captured
Runoff
Soil
Type
Flow Length
Land Cover
Rainfall
Intensity
Slope
Total Captured Runoff is compared with Reservoir Capacity and estimated losses to evaporation (monthly)…
You can only capture what you can use
or hold!

## Slide 49
Captured Rainfall
+ Additions
Blue Water

## Slide 50
Green Water Volume
Grey Water Volume
+ Blue Water Volume
Total Water Volume
380 m gallons / yr
30 m gallons / yr
50 m gallons / yr
300 m gallons / yr
Example Estimated Calculations
For entire catchment area!

## Slide 51
(Total Water Volume per year)(Length of Production Cycle)
(Plant Density)
(Total Production Area)
From Total Water Volume
=> Per Plant Consumptive Water Use:

## Slide 52
Chart: 
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Green Blue Grey | 10.4983 | 119.1538 | 12.2064
Water Volume of Consumptive Use
Characterized by Water Type
9.97 gallons
8.01 gallons
98.34 gallons
Ex. #3 Container Buxus (U.S. East Coast)
Green Water Volume
Grey Water Volume
Blue Water Volume
Total = 116.32 gallons

## Slide 53
Water Volume of Consumptive Use Characterized by Production Use
5.60 gallons
6.41 gallons
18.52 gallons
Ex. Greenhouse 72 Cell Tray
Misting (4 weeks)
Swamp Cooler (12 Weeks)
Ebb & Flood (8 Weeks)
Chart: 
 | 6.4106 | 5.6027 | 18.5185
Total = 30.53 gallons

## Slide 54
What about scarcity?

## Slide 55: Water Volume vs. Weighted Water Volume
Appropriate for comparing changes in water use efficiency from system changes
  irrigation schedule
  recycling techniques
Appropriate for comparing system efficiencies among similar systems with variable water scarcity.
Appropriate for comparing environmental impacts across systems with variable water scarcity.
Appropriate for quantifying environmental impact to location throughout year.
Moving Target! … Changes with shifting climate (availability) and use changes.

## Slide 56: How is scarcity calculated?
Multiple methods, attempting to answer the question
“What is the potential to deprive another freshwater user—human or ecosystem—by consuming freshwater in this region?”
Generally expressed as in range between .01 and 100.

## Slide 57: How is scarcity calculated?
Withdrawal-to-Availability ratio (WTA) ~2008 (early)
Consumption-to-Availability ratio (CTA) ~2012 (common)
Inverse of Availability minus Demand (AWARE) ~2017 (new)
Generally expressed as in range between
.01 ---------------------------------------------- 100
Low scarcity
(water abundance)
High scarcity
(water limited)
Calculation Methods

## Slide 58: Selected Water Scarcity Indices (2011)
A Water Scarcity Index is a ratio equal to CONSUMPTIVE WATER USE
AVAILABILITY
1.0 = All Available Water is Being Used

## Slide 59
x Monthly Scarcity Index
∑
Monthly Water Volume (Blue + Grey)
Marketable Plants in Production Area
+
Green Water Volume
Marketable Plants in Production Area
( )
Weighted Water Footprint =

## Slide 60
Embodied WF
Green WF
Blue WF
Grey WF
Blue WF from Reservoir Evaporation
Blue WF from Irrigation Events
Example: Preliminary WF of a single, marketable #3 Container Holly, East Coast U.S.
21.1 gal
18.9 gal
3.5 gal
4.2 gal
11.1 gal
7.8 gal
Total: 47.7 Weighted Gallons

## Slide 61
Technologies and Practices
What is pushing development/implementation?
Droughts
Increased Competition for Water
Regulation
  Runoff capture/control from irrigated agriculture
    (CA, FL, MD, OR, TX)
  Waste Discharge Permits for Nurseries (CA)
  Numeric Nutrient Criteria / N and P Limits (FL)
  Chesapeake Bay Watershed – Total Maximum Daily Load (WV, VA, MD, DE, PA, NY)

## Slide 62
Nutrient contaminants
Algae
Aquatic weeds
Duckweed so thick, birds walk on it…

## Slide 63
Pesticide contaminants

## Slide 64
Herbicide/Growth regulator contaminants
Imprelis phytotoxicity
Cycocel phytotoxicity

## Slide 65
Pathogen contaminants
Waterborne pathogens
  perennial problem
  billions in crop losses
Photo: E. Nyberg
Sporangia (Phytophthora nicotianae) release of zoospores into irrigation water can lead to plant infection.
Chemically-based treatment systems are effective, but have
significant upfront costs
operational expenses
worker safety issues
Potential for environmental harm

## Slide 66
Conserving
Recycling
Remediating

## Slide 67
Conservation
Generally, applying less water through irrigation strategies and systems.
“dry” nursery
ET replacement
irrigating at night
Drip irrigation

## Slide 68
Recycling
Capturing and conditioning irrigation water for re-use:
Ebb/Flood
Channels/Drainage/Ponds
Chlorination for pathogens
Filtration for herbicides/Growth regulators

## Slide 69
Remediation
Capturing and conditioning used irrigation water for return to the environment/community:
Channels/Drainage/Ponds
Filtration for herbicides
Reducing nutrient loads

## Slide 70
Nursery Pad
Irrigation Pond
Catchment
Pond
Constructed
Wetland

## Slide 71
Types of Ponds
Sedimentation Ponds / Catch Basins
Routing runoff through control structures to limit sediment movement

## Slide 72
Types of Ponds
Constructed Wetland
“Constructed water (wetland) treatment basins”
Captures nutrients, sediment, pesticides

## Slide 73
Types of Ponds
Vegetative waterways
Captures nutrients, sediment, pesticides

## Slide 74
Wetland (water basin) functions
Soils provide habitat for microbes
Microbes process
  nutrients
  organic contaminants
Vegetation slows water
Plant uptake/absorption
  nutrients
  trace metals
  other compounds

## Slide 75
Shallow 6” to 15” freshwater marsh
Retain water for 3-3.5 days
Recommend 2’-3’ deep
For smaller footprint, can increase depth to max 4’

## Slide 76
Nitrogen results

## Slide 77
Phosphorus results

## Slide 78
Subsurface flow constructed wetlands

## Slide 79
Subsurface flow constructed wetlands
2’-deep layer of coarse medium (pea gravel)
When targeting phosphorus, instead of pea gravel, the subsurface flow lining should be a pre-screened fired-clay nugget.

## Slide 80
Phosphorus removal
Subsurface flow CWs treatment enhanced phosphorus removal
Vegetated subsurface flow wetlands increased longevity of phosphorus removal
Monitor for phosphorus saturation of clay
  Removal efficiency declines as binding sites fill, replace clay

## Slide 81
Floating wetlands (smaller scale)

## Slide 82
Floating treatment wetlands (FTWs)

## Slide 83
Sand Filtration
Rapid sand filtration
    Coarse sand (>1mm)
    Removes larger particles only
    Does not remove pathogens
    Does not remove pollutants
    18 – 180 gpm/yd2
    Low maintenance

## Slide 84
  Slow sand filtration
    Removes pathogens
    Removes many pollutants
    Low maintenance
    Slow flow rates 0.5–2 gpm/yd2
Sand Filtration

## Slide 85
Mechanism - physical
(Huisman and Wood, 1974)
http://bikonwater.com/pressure_sand.html
Adsorption/ attachment
Screening/ straining
Sedimentation

## Slide 86
Mechanism - biological
Predation, assimilation, attachment to biofilms
photo-dict.faqs.org/phrase/621/bacteria.html
Community of microorganisms
  algae
  bacteria
  diatoms
  zooplankton
“Schmutzdecke”- most treatment occurs

## Slide 87
System Design

## Slide 88
Graphic: L. Oki
Notes: 1. Captured runoff is stored in a reservoir or containment. Runoff typically occurs in surges following irrigation events or storms. A float switch monitors the water level. If there is runoff present, it is pumped to the sand filters.
2. Two sand filters are used so that when one is out of service for maintenance, the other can remain in operation. Overflow from the sand filters is returned to the reservoir.

## Slide 89
Notes: Flow control is critical for optimal treatment efficiency. The sand beds must remain submerged.
Treated water is stored for later use.

## Slide 90
Notes: The treated water is pressurized for reuse for irrigation.
If there is no runoff to be treated, cleaned water needs to return to the sand filters to maintain flows through the sand bed.

## Slide 91
Notes: 6. If there is no treated water available for irrigation, then an alternative water supply needs to be used.

## Slide 92
Installations
Photo: L. Oki
Estimated treatment capacity
Surface area ≈ 50 sq.ft. (5’x10’)
@ 0.5gpm/yd2 → 4,400 gpd
Berylwood Tree Farm, Somis, CA
Notes: Septic tanks can be used to contain the sand beds. This installation will have two of these tanks.
These tanks are estimated to contain sand beds estimated at 5’ x 10’. So, at 50 sq.ft. each, that these tanks will be able to treat 4,400 gpd @0.5gpm/yd^2 or a total of 8,800 gpd.

## Slide 93
sand calcined clay polyethylene beads
crushed brick Kaldnes®
Evaluation of Alternatives to Sand
. . . Faster water treatment rates?
Notes: *Preliminary research
Sand- Typically used
Crushed brick -Recycled material
Calcined clay- Reduces phosphorus in water by sorption
Kaldnes- moving biofilter bed, used in fisheries, used in waste water treatment ***** loook up more
Polyethylene beads- same material as Kaldnes but different physical characteristics
Hoping to find a substrate alternative to sand that is both effective at pathogen removal and has the potential for faster flow rates, or less clogging

## Slide 94
Relative colony counts
Chart: Zoospore Removal (%)
| Sand: 10cm | Brick: 10cm | Clay: 10cm | Beads: 60cm | Kaldnes®: 60cm
Day 0 | 77.665 | 63.866 | 44.63 | 33.448 | 37.767
Day 21 | 99.089 | 93.69 | 92.548 | 86.145 | 63.909
Flow Rate = 30 mL/min
Notes: This data set shows the removal of Phytophthora capsici from the runoff water. The lighter colored bars indicate the reference quantity of colony forming units prior to treatment and the darker bar represents the sample below the sand bed (post treatment). The date runoff was introduced to the filters is 5/3 and the reduction in the height of the bars below the reference bar indicates removal of the pathogen. This data shows that the biofilms take about 15 days to fully develop. Sand still the best, especially at first. After biofilm forms, brick, clay and beads are still very good.

## Slide 95
Conclusions
Biological treatment systems:
Require little or no inputs
  Contrast with energy (UV irradiation) or chemical-based (chlorination) methods
Can remove nutrients, chemical pollutants, and pathogens

## Slide 96
Conclusions
Land use for treatment systems instead of production
Slow sand filtration
Low flow rates: storage of large volumes of water
Constructed wetlands
Higher flow rates: adequate retention time for treatment

## Slide 97
Conclusions – Slow Sand Filter
Both vegetated and slow sand systems require long residence times
Slow sand filters can clog if water contains particulates
Efficient water treatment systems may consist of combinations of treatment methods
  Vegetated or slow sand systems alone can provide adequate treatment
  Paired systems may be able to provide greater flow rates

## Slide 98
Cleanwater3.org

## Slide 99
Granular Activated Carbon (GAC)
U.F. Experiment
Grower Location Experiment

## Slide 100
  Active ingredient in Bonzi, Paczol, Piccolo, Piccolo 10XC.
  Compact plants
Applied as spray or drench typically 1-200 ppm
Active in ppb range. 6 month half-life in water
The Plant Growth Regulator Paclobutrazol
50 ppb
10 ppb
5 ppb
Levels found in ponds & tanks

## Slide 101
No filter
12 sec
GAC filtration
No filter
59 sec
GAC
filtration
Paclobutrazol at 50 ppb
No Paclo
Increasing GAC contact time increases paclobutrazol removal: Begonia test

## Slide 102
Grower Location
Ornamental greenhouse operation
  3 GAC Filters in series
  Tank Volume: 264 gal
  17 to 50 gal/min flow rate
  Minimum Contact time: 3.3 min/filter (10+ min total)

## Slide 103
Three crop cycles varied in paclo application rate
Chart: Week #
| 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 44
Pre. GAC Filtration | 11.5 | 4.2 | 15.5 | 7.2 | 2 | 23 | 23 | 8.75 | 7.75 | 3.75 | 14.25 | 12 | 20 | 72.5 | 19.25 | 56.8 | 28.5 | 14.3 | 3.25 | 4.75 | 0.75 | 3.5 | 6.5 | 8.25 | 3.2 | 3.75 | 1.5 | 0.5 | 0.25 | 0.5 | 1 | 0.25
Post GAC Filtration | 0.5 | 0 | 0.3 | 0.1 | 0.3 | 0.25 | 0.25 | 0.25 | 0 | 0 | 3.25 | 0.25 | 0.5 | 1.25 | 0.75 | 0.75 | 0 | 0.5 | 1 | 0.5 | 0.25 | 0 | 0.25 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 105
GAC Conclusions
Design for 15:1 volume to flow (for example, 1500 gal filter for 100 gal/min gives 15 minute contact time)
Cost for 50 gal/min GAC filter in 20-acre ebb-and-flood system:
Item | Capital | Per Year
GAC filter | $20,800 | $2,800
Pump & pre-filter | $6,600 | $660
GAC (one change/year) | $2,550 | $2,550
Labor for maintenance (3 h/week @ $25) |  | $3,990
Monthly test paclo before & after filter @ $70/sample |  | $1,680
Total | $29,950 | $11,680

## Slide 106
visit cleanwater3.org & NCER.ca.uky.edu www.facebook.com/ReduceRemediateRecycle/
Notes: Clean WateR3 is federally funded by the USDA-Specialty Crops Research Initiative in partnership with the Water Education Alliance for Horticulture.
Subscribe to newsletter.